## Slide 1: Adsorbing Hemoglobin in Column Flow Experiments – diff Eq analysis

## Slide 2: Background – Ex-vivo experiments
Columns are set up in PBS, tube primed with whole rat blood
Flow starts, outflow collected as sample per minute
Plasma hemoglobin concentration measured for haptoglobin-immobilized beads and control

## Slide 3: Data
Capture region

## Slide 4: Kinetics
B = Hemoglobin in plasma – haptoglobin-bound bead group
P = Available haptoglobin on bead surface
C = Hemoglobin in plasma –control group
BP = Adsorbed hemoglobin-haptoglobin complex
0-D “reactor” kinetics:
]

## Slide 5: Primary model
Method: minimizing error function of d[C]/dt to get values for s and , assigning those as starting guesses for s and µ. Then, minimizing system for sB, yB, µB, zB, and rB.
Var. | Type | Significance | Value & units
t | IV | Time | 1-24 min
P | DV | Available bound haptoglobin | I.C.: 1.35E-05 mol/dL
B | DV | Plasma hemoglobin in study group (SG) | I.C.: -3.35E-07 mol/dL
C | DV | Plasma hemoglobin in control group (CG) | I.C.: -3.80E-07 mol/dL
kr | OP | Reaction rate constant | 1.52E05 dL/(mol*s)
sB | OP | Saturation value in SG | 4.57E-05
yB | OP | Time scale in SG | 4.36E-01
µB | OP | Time shift in SG | 3.64E00 s
zB | OP | Model adjustment in SG | 4.52E00
rB | OP | Model adjustment in SG | 1.48E00
s | OP | Saturation value in CG | 1.38E-05
µ | OP | Time shift in CG | 7.00E00 s

## Slide 6: Accuracy of model

## Slide 7: Other attempted model

## Slide 8: Bifurcation analysis
Stable
Unstable

## Slide 9
Bifurcation analysis Continued
Solutions follow extremely different paths over the test time range when parameters are bifurcated
Steadystates are most often found by 0 concentration – reaction is extremely stable when nothing happens

## Slide 10: Parametric sensitivity
Effect of kr on model solution, +/- 50%
Sensitivity of Study Group Hemoglobin to different parameters

## Slide 11: Limitations & next steps
Model needs refinement – close but not quite
Incorporate original unmodified data to include hemolysis term in analysis
Investigate importance of kr and previous analyses
Attempt analytical solution of concentration via transport & use better sigmoidal solution

## Slide 12: THANK YOU
Work made possible by:
Dr. William Federspiel
Dr. Nahmah Kim-Campbell
Anna Maywar